Basic Image Transformations

cvtColor
converts an image from one color space to another

cvtColor(src, dst, code);

src	input image
dst	output image

code	COLOR_BGR2GRAY, COLOR_BGR2YCrCb, COLOR_BGR2HSV etc.

imwrite
save picture

imwrite("name.jpg", src);

resize

resize(src, dst, dsize, fx, fy);

dsize	output image size e. g. Size()
fx	scale factor along the horizontal axis e. g. 0.5
fy	scale factor along the vertical axis e. g. 0.5

smooth
- leaving out noise or other fine-scale structures/rapid phenomena
- perform a smoothing operation we will apply a filter to an image
- an output pixel's value (i.e. g(i,j)) is determined as a weighted sum of input pixel values (i.e. f(i+k,j+l)) : g(i,j)=∑f(i+k,j+l)h(k,l)
- h(k,l) is called the kernel, which is nothing more than the coefficients of the filter
- visualize a filter as a window of coefficients sliding across the image.

GaussianBlur(src, dst, ksize , sigmaX, sigmaY);

ksize	Gaussian kernel size. e. g. Size(15, 15)
sigmaX	Gaussian kernel standard deviation in X direction e. g. 0
sigmaY	Gaussian kernel standard deviation in Y direction e. g. 0

rotate

transpose(src, dst);

warpAffine
warpAffine transforms the source image using a specified matrix
Mat matRotation = getRotationMatrix2D(Point( 0,100 ), (200 - 180), 50 / 50.0 );	//center, angle, scale
warpAffine(src, dst, InputArray, dsize, flags, borderMode, borderValue);

InputArray	2×3 transformation matrix e. g. matRotation
dsize	size of the output image e. g. src.size()
flags	combination of interpolation methods e. g. INTER_LINEAR
borderMode	pixel extrapolation method e. g. 0
borderValue	value used in case of a constant border e. g. Scalar()

morphology transformations
- morphological operations apply a structuring element to an input image and generate an output image
- the most basic morphological operations are two: erosion and dilation
- uses: removing noise, isolation of individual elements and joining disparate elements in an image.

original	dilate	erode

threshhold
- fixed-level thresholding to a single-channel array
- used to get a bi-level (binary) image out of a grayscale image
- removing a noise, filtering out pixels

threshold(src, dst, thresh, maxval, type);

thresh	threshold value
maxval	maximum value
type	THRESH_BINARY, THRESH_BINARY_INV, THRESH_TRUNC, THRESH_TOZERO, THRESH_TOZERO_INV, THRESH_MASK THRESH_OTSU, THRESH_TRIANGLE

canny edge detector
- convolutions are used to compute derivatives in an image
- notice that in an edge, the pixel intensity changes
- gradient indicates a major change in the image
- appear as maximum/minimum at the first derivative
Canny(src, dst, thresh, maxval, apertureSize);
thresh	threshhold value
maxval	maximum value
apertureSize	aperture size for the Sobel operator

additional
compare to other edge detectors
Contour Properties and Singing Leaves

contours
- Contours can be explained simply as a curve joining all the continuous points (along the boundary), having same color or intensity
- useful tool for shape analysis and object detection and recognition
- before finding contours, apply threshold or canny edge detection

vector<vector<Point> > contours;
findContours(src, contours, mode, method);

src	binary image with applied threshhold and edge detection
contours	detected contours: each one is stored as a vector of points
mode	mode of the contour retrieval algorithm: RETR_EXTERNAL, RETR_LIST, RETR_CCOMP, RETR_FLOODFILL

method	contour approximation algorithm: CHAIN_APPROX_NONE, CHAIN_APPROX_SIMPLE, CHAIN_APPROX_TC89_L1, CHAIN_APPROX_TC89_KCOS

drawContours(dst, contours, contouridx, color, thickness, lineType)

contouridx	parameter indicating a contour to draw
color	e. g. Scalar(255, 255, 255)1, 8, vector<Vec4i>()
thickness	thickness of lines the contours are drawn with. If it is negative (for example, thickness=CV_FILLED ), the contour interiors are drawn.

lineType	default=8

contourArea, arcLength, boundingRect, minEnclosingCircle, moments, HuMoments

tasks

usage of main and sub function

Find leave contour
- open leave image from Pictures/database
- resize it for a better view
- threshold, erode, edge detection with canny
- findContours, print out number
- drawCountours
- exclude small contours (→ area), print our new number
Calculate numbers for singing leaves
- calculate moments and mass point
- calculate distance between mass point and contour points
- mix distances (random_shuffle)
Save distances to file
open .yaml file and save values

Convert image/contour into music
- https://ojack.github.io/PIXELSYNTH/
- http://www.musicalgorithms.org/3.2/#howto
Additional
find approximated contour, bounding Rectangle, minimum enclosing circle
Shape Matching

compare shapes of different leaves

- declare main and sub function
- threshold and find edges in an input image
- find contours, delete too small ones
- calculating the HuMoments
- match the shape to another processed image → matchShapes()

Key Points

compare different leaves

find better threshold, settings for the recognition

Remove dirt from microscopic images

You have different micrsocopic images with and without cells with some dirt on the lense.
Try to remove the dirt from the images with the cells.